## Slide 1
W01·B On the network
CSC 436 — Web Application Systems
1 / 37
CSC 436 — Web Application Systems
Getting on the network
How a machine acquires an identity, finds its neighbours, and reaches everything else — and why none of it is visible from your source code
Week 1 · Block B
30 minutes
Updated 2026-09-05

## Slide 2
W01·B On the network
CSC 436 — Web Application Systems
2 / 37
Fictional CampusPulse case: reachable from here, invisible from there
Maya's laptop
DHCP assigns 10.24.18.73/20
The gateway is 10.24.16.1; DNS is 10.20.0.53
CampusPulse answers at localhost:8080
Luis's laptop
curl to 10.24.18.73:8080 gets connection refused
The listener table reveals 127.0.0.1:8080, not the Wi-Fi address
One bind setting, not the React code, decides who can connect

## Slide 3
W01·B On the network
CSC 436 — Web Application Systems
3 / 37
Four questions, answered before your code exists
Who am I? — an address this machine is allowed to use
Who is nearby? — which addresses it can reach without help
How do I get out? — where to send everything else
Who answers names? — which server turns text into an address
◆ KEY IDEA
Your application answers none of these. It inherits all four answers, from a
server it never authenticated to, over a protocol it never chose.

## Slide 4
W01·B On the network
CSC 436 — Web Application Systems
4 / 37
Four words about joining a local network
Term | Plain meaning
DHCP | The protocol a network uses to hand a newly joined device its address and settings.
Lease | The time-limited grant of that address. It expires, is renewed, and can change.
MAC address | A hardware address burned into a network adapter. Used only within one local network.
ARP | The "who has this address?" question a device shouts locally to find a neighbour's MAC address.
◆ KEY IDEA
DHCP gives a new device its starting information. ARP then helps it find another device on the same local network.

## Slide 5
W01·B On the network
CSC 436 — Web Application Systems
5 / 37
Four words about choosing the next hop
Term | Plain meaning
Subnet mask | The rule that says which addresses count as local neighbours and which do not.
CIDR (/20) | A shorthand for that same rule: how many leading bits of the address identify the network.
On-link | A destination you can reach directly, without asking the gateway to forward it.
Gateway | The device you hand traffic to when the destination is not on-link.
◆ KEY IDEA
Every mechanism in the next fifteen minutes is one of these eight words in action. You are not expected to know them yet.

## Slide 6
W01·B On the network
CSC 436 — Web Application Systems
6 / 37
What your machine will tell you
Windows ipconfig /all - captured and sanitized CONSOLE
Physical Address. . . . . : 00-0D-3A-XX-XX-XX # layer 2 identity
DHCP Enabled. . . . . . . : Yes # <- negotiated
IPv4 Address. . . . . . . : 10.0.20.252 # 1. who am I
Subnet Mask . . . . . . . : 255.255.128.0 # 2. who is nearby
Default Gateway . . . . . : 10.0.0.1 # 3. how do I get out
DHCP Server . . . . . . . : 168.63.129.16 # who told me all this
DNS Servers . . . . . . . : 10.0.254.4 # 4. who answers names
◆ KEY IDEA
Gateway, DHCP server, resolver: three different jobs. A home router may do
all three, but they need not share an address.
Course — full annotated capture · Microsoft — what 168.63.129.16 is
Notes: SOURCES: Course — [full annotated capture](../samples/network-config.txt) Microsoft — [what 168.63.129.16 is](https://learn.microsoft.com/en-us/azure/virtual-network/what-is-ip-address-168-63-129-16)

## Slide 7
W01·B On the network
CSC 436 — Web Application Systems
7 / 37
Windows: inspect the active connection
Windows PowerShell - any directory; read-only POWERSHELL
ipconfig /all
Get-NetIPConfiguration
◆ KEY IDEA
Find the active adapter's address, prefix or mask, gateway, and DNS servers. Do not copy the sample's addresses.
Microsoft — Get-NetIPConfiguration
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. ipconfig /all Get-NetIPConfiguration SOURCES: Microsoft — [Get-NetIPConfiguration](https://learn.microsoft.com/powershell/module/nettcpip/get-netipconfiguration)

## Slide 8
W01·B On the network
CSC 436 — Web Application Systems
8 / 37
macOS: find the interface and address
macOS Terminal - Bash/zsh; any directory; read-only BASH
networksetup -listallhardwareports
printf 'Device for active Wi-Fi/Ethernet (from list): '
read -r iface
ipconfig getifaddr "$iface"
ipconfig getpacket "$iface"
ifconfig "$iface"
◆ KEY IDEA
Do not assume Wi-Fi is en0. Match the hardware port to its Device entry.
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. networksetup -listallhardwareports printf 'Device for active Wi-Fi/Ethernet (from list): ' read -r iface ipconfig getifaddr "$iface" ipconfig getpacket "$iface" ifconfig "$iface"

## Slide 9
W01·B On the network
CSC 436 — Web Application Systems
9 / 37
macOS lease fields: the same questions
These fields describe the last IPv4 DHCP response, not every current policy.
Field in getpacket | Same question as the Windows capture
yiaddr | Which IPv4 address was supplied?
subnet_mask | Which destinations are local?
router | Which gateway was supplied?
domain_name_server | Which name servers were supplied?

## Slide 10
W01·B On the network
CSC 436 — Web Application Systems
10 / 37
macOS: find the gateway and resolvers
macOS Terminal - Bash/zsh; any directory; read-only BASH
route -n get default
scutil --dns
◆ KEY IDEA
Read gateway and interface in the route; read nameserver and scope in the resolver configuration.
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. route -n get default scutil --dns

## Slide 11
W01·B On the network
CSC 436 — Web Application Systems
11 / 37
How the address arrives: DISCOVER, OFFER, REQUEST, ACK
DHCP DORA — four messages, two of them broadcast, before the machine has an address to be addressed by
IETF — RFC 2131 §3.1, DHCP client-server interaction
Notes: SOURCES: IETF — [RFC 2131 §3.1, DHCP client-server interaction](https://www.rfc-editor.org/rfc/rfc2131.html)

## Slide 12
W01·B On the network
CSC 436 — Web Application Systems
12 / 37
The lease is not just an address
Address + mask — identity, and the definition of "nearby"
Default gateway — the way out
DNS servers — who resolves names, which is a trust decision made for you
Lease duration — this is a rental, and it expires
NTP, domain, search suffix, routes — options nobody reads until one breaks
▲ WATCH OUT
A lease that never expires is not normal. On the capture above it ran to the year
2162 — a platform artifact of a cloud VM. A home router hands out 12 or 24 hours.

## Slide 13
W01·B On the network
CSC 436 — Web Application Systems
13 / 37
ARP: the frame needs a different address
The problem
The packet is addressed to 10.0.19.7. The frame needs a MAC.
So the host broadcasts "who has 10.0.19.7?" and caches the reply.
The reality on a cloud network
Real arp -a: 10.0.0.1, 10.0.0.63, 10.0.1.52, 10.0.7.77 — all four
map to the same MAC.
No shared wire; the fabric answers for everything.
▸ NOTE
IPv6 replaces ARP with NDP. Same job.
IETF — RFC 826, Address Resolution Protocol · RFC 4861, Neighbor Discovery
Notes: SOURCES: IETF — [RFC 826, Address Resolution Protocol](https://www.rfc-editor.org/rfc/rfc826.html) · [RFC 4861, Neighbor Discovery](https://www.rfc-editor.org/rfc/rfc4861.html)

## Slide 14
W01·B On the network
CSC 436 — Web Application Systems
14 / 37
Which addresses can exist in public
CIDR | Where it works | You will meet it
10.0.0.0/8 | private only | cloud VNets, campus
172.16.0.0/12 | private only | Docker, WSL
192.168.0.0/16 | private only | home routers
127.0.0.0/8 | this machine only | the whole problem
169.254.0.0/16 | link-local | DHCP failed; cloud metadata
fe80::/10 | link-local IPv6 | every IPv6 interface
IETF — RFC 1918, private address allocation · RFC 3927, IPv4 link-local
Notes: SOURCES: IETF — [RFC 1918, private address allocation](https://www.rfc-editor.org/rfc/rfc1918.html) · [RFC 3927, IPv4 link-local](https://www.rfc-editor.org/rfc/rfc3927.html)

## Slide 15
W01·B On the network
CSC 436 — Web Application Systems
15 / 37
CIDR: how many bits are the network?
255.255.128.0 is /17 — worked from the real capture TEXT
255.255.128.0 = 11111111 11111111 1000 0000 00000000
|--- 17 network ---|---- 15 host ----|
2^15 = 32,768 addresses 10.0.0.0 -> 10.0.127.255
10.0.19.7 in the /17 -> on-link, ARP for it
10.0.200.4 NOT in the /17 -> hand it to the gateway
8.8.8.8 nowhere near -> hand it to the gateway
◆ KEY IDEA
The mask is the if-statement your machine runs on every outbound packet: on-link, or hand it to the gateway?

## Slide 16
W01·B On the network
CSC 436 — Web Application Systems
16 / 37
The route table is that if-statement
Windows route print -4 - trimmed; most specific prefix wins CONSOLE
Destination Gateway Meaning
0.0.0.0/0 10.0.0.1 default route
10.0.0.0/17 On-link local campus subnet
127.0.0.0/8 On-link loopback
169.254.169.254/32 10.0.0.1 one pinned host
to 10.0.19.7 -> /17 -> ARP for it directly
to 8.8.8.8 -> /0 -> frame to gateway; IP stays 8.8.8.8
to 127.0.0.1 -> /8 -> never leaves the kernel
Course — annotated route table
Notes: SOURCES: Course — [annotated route table](../samples/network-config.txt)

## Slide 17
W01·B On the network
CSC 436 — Web Application Systems
17 / 37
Windows: routes and nearby addresses
Windows PowerShell - any directory; inspection only POWERSHELL
route print -4
arp -a
Get-NetNeighbor -AddressFamily IPv6
◆ KEY IDEA
Routes choose the next hop. Neighbor entries map nearby network addresses to link addresses.
Microsoft — Get-NetNeighbor
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. route print -4 arp -a Get-NetNeighbor -AddressFamily IPv6 SOURCES: Microsoft — [Get-NetNeighbor](https://learn.microsoft.com/powershell/module/nettcpip/get-netneighbor)

## Slide 18
W01·B On the network
CSC 436 — Web Application Systems
18 / 37
macOS: routes and nearby addresses
macOS Terminal - Bash/zsh; any directory; inspection only BASH
netstat -rn -f inet
route -n get default
arp -a
ndp -an
◆ KEY IDEA
Compare Destination, Gateway, and Netif; use ARP for IPv4 neighbors and NDP for IPv6.
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. netstat -rn -f inet route -n get default arp -a ndp -an

## Slide 19
W01·B On the network
CSC 436 — Web Application Systems
19 / 37
Four words about reaching the Internet
Term | Plain meaning
Private address | An address usable only inside one network. Many networks reuse the same private ranges.
Public address | A globally unique address that the rest of the Internet can route to.
NAT | Rewriting private addresses into one shared public address on the way out, and back on the way in.
Port | A number that says which program on a machine a message is for.
◆ KEY IDEA
A home or campus network can use private addresses inside, then use NAT to share one public address when it talks to the Internet.

## Slide 20
W01·B On the network
CSC 436 — Web Application Systems
20 / 37
Four words about a program's connection
Term | Plain meaning
Socket | One end of a conversation: an address plus a port.
Listening socket | A program waiting for connections on a port.
Connected socket | An established conversation between two specific address-and-port pairs.
Bind address | The address a program agrees to accept connections on. 127.0.0.1 means "this machine only".
◆ KEY IDEA
127.0.0.1 (also called localhost, or loopback) never leaves your machine. 0.0.0.0 means "accept on every address I have".

## Slide 21
W01·B On the network
CSC 436 — Web Application Systems
21 / 37
NAT: the address you have is not the address you are
One public address, many private machines, and a translation table only you can open

## Slide 22
W01·B On the network
CSC 436 — Web Application Systems
22 / 37
The same request, from both ends
 | this host believes | the server received
address | 10.0.20.252 | 203.0.113.181
port | 49302 | 55346
■ THIS BREAKS PRODUCTION
Address and port were rewritten in flight — and a second run seconds later left
from
203.0.113.183. The egress is a pool, not a box.
Course — the full NAT capture · IETF — RFC 3022, Traditional NAT and NAPT
Notes: SOURCES: Course — [the full NAT capture](../samples/path-and-nat.txt) IETF — [RFC 3022, Traditional NAT and NAPT](https://www.rfc-editor.org/rfc/rfc3022.html)

## Slide 23
W01·B On the network
CSC 436 — Web Application Systems
23 / 37
Ports and sockets: two tuples, and the difference matters
A listening socket is (address, port) — two values, e.g. 0.0.0.0:8471
A connected socket is (local addr, local port, remote addr, remote port) — four
The four-tuple is why one server port serves thousands of clients unambiguously
The client never chose its port; the kernel took one from the ephemeral range
TIME_WAIT is that four-tuple being held after close, not a leak
◆ KEY IDEA
A socket is an address and a port. If you got the address wrong, the port was
never the problem.

## Slide 24
W01·B On the network
CSC 436 — Web Application Systems
24 / 37
One listener, many conversations
netstat -ano, captured during a live request CONSOLE
Proto Local Address Foreign Address State
TCP 0.0.0.0:8471 0.0.0.0:0 LISTENING 25224
TCP 10.0.20.252:62681 10.0.20.252:8471 TIME_WAIT 0
TCP 10.0.20.252:62684 10.0.20.252:8471 TIME_WAIT 0
TCP 127.0.0.1:62630 127.0.0.1:8471 TIME_WAIT 0
row 1 TWO values: (0.0.0.0, 8471) <- the listener
rows 2+ FOUR values: (local, 62681, remote, 8471)
server side identical; the CLIENT ports differ
Course — full socket capture
Notes: SOURCES: Course — [full socket capture](../samples/sockets-and-ports.txt)

## Slide 25
W01·B On the network
CSC 436 — Web Application Systems
25 / 37
One machine, one port, two answers
only the bind address changes CONSOLE
# bound to 127.0.0.1
TCP 127.0.0.1:8471 LISTENING
curl 127.0.0.1:8471 -> campuspulse ok
curl 10.0.20.252:8471 -> Connection refused (same box)
# rebound to 0.0.0.0 — no code changed
TCP 0.0.0.0:8471 LISTENING
curl 127.0.0.1:8471 -> campuspulse ok
curl 10.0.20.252:8471 -> campuspulse ok
Course — the full transcript
Notes: SOURCES: Course — [the full transcript](../samples/sockets-and-ports.txt)

## Slide 26
W01·B On the network
CSC 436 — Web Application Systems
26 / 37
▶ LIVE DEMO
Break it live, in ninety seconds
DO THIS
Open A and B at the repo root; choose your OS steps; Node 18+
Run the loopback-only server and the two requests on the next slides
Stop it, bind all interfaces, and repeat without changing the URL
WATCH FOR
Loopback: JSON; LAN request fails
Wildcard: JSON on both if allowed
IF IT FAILS
Open the socket capture on the cleanup slide.
Course — the stub server
Notes: SOURCES: Course — [the stub server](../samples/campuspulse-stub.mjs)

## Slide 27
W01·B On the network
CSC 436 — Web Application Systems
27 / 37
Windows A: bind only to loopback
Windows PowerShell - repository root; keep Terminal A running POWERSHELL
node --version
node .\weeks\week01\samples\campuspulse-stub.mjs 127.0.0.1 8471
▸ NOTE
Expect: campuspulse listening on 127.0.0.1:8471.
Course — stub arguments and response fields
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. node --version node .\weeks\week01\samples\campuspulse-stub.mjs 127.0.0.1 8471 SOURCES: Course — [stub arguments and response fields](../samples/campuspulse-stub.mjs)

## Slide 28
W01·B On the network
CSC 436 — Web Application Systems
28 / 37
macOS A: bind only to loopback
macOS Terminal - Bash/zsh; repository root; Node 18+ BASH
node --version
node ./weeks/week01/samples/campuspulse-stub.mjs 127.0.0.1 8471
◆ KEY IDEA
Expect "campuspulse listening on 127.0.0.1:8471". Keep this terminal running.
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. node --version node ./weeks/week01/samples/campuspulse-stub.mjs 127.0.0.1 8471

## Slide 29
W01·B On the network
CSC 436 — Web Application Systems
29 / 37
Windows B: ask two different addresses
Windows PowerShell - Terminal B; choose YOUR active LAN IPv4 POWERSHELL
ipconfig
$lan = Read-Host 'Active LAN IPv4, not 127.0.0.1'
Get-NetTCPConnection -State Listen -LocalPort 8471 |
Select-Object LocalAddress, LocalPort, OwningProcess
curl.exe --noproxy '*' -sS --max-time 3 http://127.0.0.1:8471/healthz
curl.exe --noproxy '*' -sS --max-time 3 "http://${lan}:8471/healthz"
$LASTEXITCODE
Microsoft — Get-NetTCPConnection · Course — socket evidence
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. ipconfig $lan = Read-Host 'Active LAN IPv4, not 127.0.0.1' Get-NetTCPConnection -State Listen -LocalPort 8471 | Select-Object LocalAddress, LocalPort, OwningProcess curl.exe --noproxy '*' -sS --max-time 3 http://127.0.0.1:8471/healthz curl.exe --noproxy '*' -sS --max-time 3 "http://${lan}:8471/healthz" $LASTEXITCODE SOURCES: Microsoft — [`Get-NetTCPConnection`](https://learn.microsoft.com/powershell/module/nettcpip/get-nettcpconnection) Course — [socket evidence](../samples/sockets-and-ports.txt)

## Slide 30
W01·B On the network
CSC 436 — Web Application Systems
30 / 37
macOS B: ask two different addresses
macOS Terminal - Bash/zsh; Terminal B; active LAN IPv4 required BASH
networksetup -listallhardwareports
printf 'Active LAN Device from list: '; read -r iface
lan=$(ipconfig getifaddr "$iface")
printf 'LAN IPv4: %s\n' "$lan"
# If blank, stop here and use the offline comparison.
lsof -nP -iTCP:8471 -sTCP:LISTEN
curl --noproxy '*' -sS --max-time 3 http://127.0.0.1:8471/healthz
curl --noproxy '*' -sS --max-time 3 "http://${lan}:8471/healthz"
printf 'exit=%s\n' "$?"
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. networksetup -listallhardwareports printf 'Active LAN Device from list: '; read -r iface lan=$(ipconfig getifaddr "$iface") printf 'LAN IPv4: %s\n' "$lan" # If blank, stop here and use the offline comparison. lsof -nP -iTCP:8471 -sTCP:LISTEN curl --noproxy '*' -sS --max-time 3 http://127.0.0.1:8471/healthz curl --noproxy '*' -sS --max-time 3 "http://${lan}:8471/healthz" printf 'exit=%s\n' "$?"

## Slide 31
W01·B On the network
CSC 436 — Web Application Systems
31 / 37
Windows A: change just the listener
Windows PowerShell - after Ctrl+C in A; repository root POWERSHELL
node .\weeks\week01\samples\campuspulse-stub.mjs 0.0.0.0 8471
▸ NOTE
Now repeat the socket query and both curl requests from the previous slide, unchanged.
▲ WATCH OUT
Use a trusted lab network. This exposes the synthetic stub on every IPv4 interface.
Course — stub server
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. node .\weeks\week01\samples\campuspulse-stub.mjs 0.0.0.0 8471 SOURCES: Course — [stub server](../samples/campuspulse-stub.mjs)

## Slide 32
W01·B On the network
CSC 436 — Web Application Systems
32 / 37
macOS A: change just the listener
macOS Terminal - Bash/zsh; after Ctrl+C in A; repository root BASH
node ./weeks/week01/samples/campuspulse-stub.mjs 0.0.0.0 8471
▸ NOTE
In B, repeat lsof and both curl requests. Expect a wildcard listener and, if policy permits, two JSON replies.
▲ WATCH OUT
Use a trusted lab network. The synthetic stub now listens on every IPv4 interface.
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. node ./weeks/week01/samples/campuspulse-stub.mjs 0.0.0.0 8471

## Slide 33
W01·B On the network
CSC 436 — Web Application Systems
33 / 37
What changed for Maya and Luis?
Observation | Mechanism | Safe conclusion
boundTo changes | The listener accepts more destination addresses | The bind configuration changed
servedOn differs | Each request chose an interface address | Same process, two local paths
peer port differs | Each client connection gets a source port | A request is not just a URL
Luis still cannot connect | Another boundary may block ingress | Check policy before changing code
Course — response fields
Notes: SOURCES: Course — [response fields](../samples/campuspulse-stub.mjs)

## Slide 34
W01·B On the network
CSC 436 — Web Application Systems
34 / 37
Windows: stop the stub, keep the evidence
Windows PowerShell - Terminal B; repository root; offline POWERSHELL
Get-Content .\weeks\week01\samples\sockets-and-ports.txt
◆ KEY IDEA
Press Ctrl+C in Terminal A to stop the all-interface listener.
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. Get-Content .\weeks\week01\samples\sockets-and-ports.txt

## Slide 35
W01·B On the network
CSC 436 — Web Application Systems
35 / 37
macOS: stop the stub, keep the evidence
macOS Terminal - Bash/zsh; Terminal B; repository root; offline BASH
cat ./weeks/week01/samples/sockets-and-ports.txt
◆ KEY IDEA
Ctrl+C in Terminal A stops the server. The saved Windows/Linux output is reference evidence, not today's Mac output.
Notes: PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. cat ./weeks/week01/samples/sockets-and-ports.txt

## Slide 36
W01·B On the network
CSC 436 — Web Application Systems
36 / 37
Why "it works on localhost" means nothing
127.0.0.0/8 is matched in the route table and handed back to the kernel
It does not cross the physical LAN, its router, or its NAT
A successful loopback request tests the app and a local path, not remote ingress
A private address needs an explicit external path; NAPT may also rewrite its port
Every one of those is a thing a reviewer, a friend testing your app, and your users are on the other side of
■ THIS BREAKS PRODUCTION
"It works on my machine" is not a lie. It is a true statement about a code path
that shares almost nothing with the one your users take.

## Slide 37
W01·B On the network
CSC 436 — Web Application Systems
37 / 37
◇ ACTIVE CHECKPOINT
10 min · Solo (4 min) → cold call (3 min) → debrief (3 min)
A service works for Priya, but not for Dev. Three artifacts. Diagnose it.
A) Priya runs: netstat -ano | findstr :8080
TCP 127.0.0.1:8080 0.0.0.0:0 LISTENING 9134
B) Dev runs: curl --max-time 5 http://192.168.1.47:8080/healthz
curl: (7) Failed to connect ... Connection refused
C) Dev runs: curl --max-time 5 http://192.168.1.47:3000/ -> 200 OK
1. What is the cause? 2. Which artifact rules out a completely broken path? 3. Priya says "let's just use port 80." What happens?
Course — supplied failure prompt and artifacts
Notes: SOURCES: Course — [supplied failure prompt and artifacts](../samples/injected-failures/failure-01-refused-from-lan/README.md)