## Slide 1
W01·A Short review
CSC 436 — Web Application Systems
1 / 90
CSC 436 — Web Application Systems
Course Intro and the Network Underneath
Review, preparation, logistics, teaching, individual practice, and the end-of-class brief
Week 1 · Full session
180 minutes
Updated 2026-09-05
Notes: DELIVERY: review; source Block A, slide 1.

## Slide 2
W01·A Short review
CSC 436 — Web Application Systems
2 / 90
Two laptops, one destination
◆ KEY IDEA
An illustrative classroom scenario: one simple goal, many cooperating systems.
Maya's Mac
Joins the classroom Wi-Fi
Enters https://www.depaul.edu
Opens the home page and follows a link
Luis's Windows laptop
Joins the same classroom Wi-Fi
Enters the same web address
Wants the same usable page
Notes: DELIVERY: review; source Block A, slide 2.

## Slide 3
W01·A Weekly logistics
CSC 436 — Web Application Systems
3 / 90
Where the course rules live
The syllabus is the rulebook. Schedule, grading, deadlines, and policies live there, and we walk through it separately today
These slides never replace it. If a slide and the syllabus ever disagree, the syllabus wins
Two companion documents: the AI-use policy, and the evidence standard that defines what counts as proof in this course
Unresolved questions go to the discussion board, so an answer is written down once for everybody
✦ TIP
Logistics questions: now, before we start the journey. After this slide we are on the technical material.
Course — syllabus · AI use policy · evidence standard
Notes: DELIVERY: logistics; source Block A, slide 3. SOURCES: Course — [syllabus](../../../docs/new_syllabus.md) · [AI use policy](../../../docs/ai-use-policy.md) · [evidence standard](../../../docs/evidence-standard.md)

## Slide 4
W01·A The whole journey
CSC 436 — Web Application Systems
4 / 90
The map we will keep coming back to
A fresh visit, grouped into five stages. Later slides unpack the jobs inside each stage.
Notes: DELIVERY: content; source Block A, slide 4.

## Slide 5
W01·A The whole journey
CSC 436 — Web Application Systems
5 / 90
Four words about where your request goes
Word | What it means, in one sentence
Network | A set of connected devices that can send messages to each other.
The Internet | An enormous collection of networks that agreed to pass each other's messages.
IP address | The numeric address a device uses on a network, so replies can find their way back.
Gateway (router) | The device on your network that forwards traffic to destinations outside it.
◆ KEY IDEA
These words name the route a request takes: your computer starts on one network, and its gateway sends it toward another.
Notes: DELIVERY: content; source Block A, slide 5.

## Slide 6
W01·A The whole journey
CSC 436 — Web Application Systems
6 / 90
Four words about what your request asks for
Word | What it means, in one sentence
Domain name | The human-friendly name of a site, such as www.depaul.edu.
Client and server | The client asks for something (your browser); the server answers (the website's computer).
HTTP / HTTPS | The rules browsers and servers use to ask for and return pages. HTTPS is the private version.
Resource | Any single item a page is made of: the page text, an image, a font, a stylesheet.
◆ KEY IDEA
None of these words describe how anything works yet. They are labels for the parts, so the story below has names to use.
Notes: DELIVERY: content; source Block A, slide 6.

## Slide 7
W01·A The whole journey
CSC 436 — Web Application Systems
7 / 90
1. Join a local network
◆ KEY IDEA
"Connected to Wi-Fi" means a local connection exists. It does not prove the website works.
On the computer
Choose Wi-Fi, or connect a network cable
The network adapter establishes a local connection
Supply a password or sign-in if required
On the local network
An access point or switch connects the device
Network policy decides what access is permitted
Some networks require an additional sign-in page
Notes: DELIVERY: content; source Block A, slide 7.

## Slide 8
W01·A The whole journey
CSC 436 — Web Application Systems
8 / 90
2. The computer gets its bearings
A local connection still needs usable network settings.
Information | The question it answers
This device's address | Where should replies go?
Local destinations | Which neighbors can I reach directly?
Default gateway | Who helps me reach other networks?
Name-lookup service | Who helps find the website's address?
◆ KEY IDEA
"Settings" here means four answers your computer needs before it can talk to anything: who it is, who is nearby, who forwards its traffic outward, and who translates names into addresses.
Notes: DELIVERY: content; source Block A, slide 8.

## Slide 9
W01·A The whole journey
CSC 436 — Web Application Systems
9 / 90
3. Tell the browser where you want to go
◆ KEY IDEA
That whole line is a URL — a web address. It names the rules to use (https), the site to talk to (www.depaul.edu), and optionally which page (nothing here, so: the home page).
The browser interprets the address before asking for the page.
Notes: DELIVERY: content; source Block A, slide 9.

## Slide 10
W01·A The whole journey
CSC 436 — Web Application Systems
10 / 90
4. Find an address for the name
◆ KEY IDEA
The name-lookup service is called DNS, the Domain Name System: a directory that turns a name people can remember into an address machines can use. Looking up the address is not the same job as downloading the page.
The computer asks
The human-friendly name is www.depaul.edu
Communication needs a network destination
The browser or operating system may already know a usable answer
A lookup service helps
If needed, it finds an address for the name
There may be more than one usable address
Answers can change while the familiar name stays the same
Notes: DELIVERY: content; source Block A, slide 10.

## Slide 11
W01·A The whole journey
CSC 436 — Web Application Systems
11 / 90
5. Get from the laptop to the way out
For a remote website, the computer hands outgoing traffic to a local gateway.
Notes: DELIVERY: content; source Block A, slide 11.

## Slide 12
W01·A The whole journey
CSC 436 — Web Application Systems
12 / 90
6. Networks carry the conversation
One visit crosses several networks, not a direct wire.
Part of the path | Its job
Local network | Carry traffic to the way out
Gateway | Cross the network boundary and route replies
Internet routers | Forward toward the destination
Website's network | Deliver traffic to the web service
MDN — How does the Internet work?
Notes: DELIVERY: content; source Block A, slide 12. SOURCES: MDN — [How does the Internet work?](https://developer.mozilla.org/en-US/docs/Learn_web_development/Howto/Web_mechanics/How_does_the_Internet_work)

## Slide 13
W01·A The whole journey
CSC 436 — Web Application Systems
13 / 90
7–8. Start a conversation, then ask
◆ KEY IDEA
Being able to talk to the site and asking for a particular page are different steps. HTTPS means the conversation is scrambled in transit, so people between you and the site can see that you are talking to it, but not what you sent.
Get ready to talk
The browser reaches a service for the website
For this HTTPS visit, it prepares a private conversation with the intended site
A previously established conversation may be reusable
Ask for the page
The browser requests the site's home page
It can include context such as a language preference or a previous visit
The service decides how to answer
Notes: DELIVERY: content; source Block A, slide 13.

## Slide 14
W01·A The whole journey
CSC 436 — Web Application Systems
14 / 90
9. The website's front door decides
An illustrative website architecture, not a verified diagram of DePaul's current deployment.
Notes: DELIVERY: content; source Block A, slide 14.

## Slide 15
W01·A The whole journey
CSC 436 — Web Application Systems
15 / 90
10. The application may need information
◆ KEY IDEA
The browser normally talks to the web service, not directly to the service's private database.
A ready-made page
Content may already exist as a file
The service can return it without assembling new information
Not every visit requires a database query
A page assembled for a request
The application may read stored content or another service
It may check what the visitor is allowed to see
It creates a response for the browser
Notes: DELIVERY: content; source Block A, slide 15.

## Slide 16
W01·A The whole journey
CSC 436 — Web Application Systems
16 / 90
11. A response makes the return trip
A delivered response is not yet a usable page.
Participant | Next job
Web service | Send content, a new location, or a problem
Return-path networks | Carry the response back
Local network and computer | Deliver to the right device and application
Browser | Decide what to do with the response
Notes: DELIVERY: content; source Block A, slide 16.

## Slide 17
W01·A The whole journey
CSC 436 — Web Application Systems
17 / 90
12. Request the other pieces
◆ KEY IDEA
The first response is not necessarily the whole page. One visit can involve many requests. A saved copy — a cache — is a local copy kept from an earlier visit so the same item does not have to be fetched twice.
The page can ask for more
Images and fonts
Appearance rules and application code
Fresh information needed by the page
Earlier jobs can happen again
Another resource may be on another service
Some resources can be reused from saved copies
Several requests can be in progress together
Notes: DELIVERY: content; source Block A, slide 17.

## Slide 18
W01·A The whole journey
CSC 436 — Web Application Systems
18 / 90
13. The browser makes the page
◆ KEY IDEA
These four jobs have names you will use for ten weeks: HTML is the structure, CSS is the appearance, images are the media, and JavaScript is the behavior. The browser combines them into the page you see.
The browser turns received resources into a page. Work can overlap as resources arrive.
Notes: DELIVERY: content; source Block A, slide 18.

## Slide 19
W01·A The whole journey
CSC 436 — Web Application Systems
19 / 90
14. Visible is not always ready to use
◆ KEY IDEA
Our destination is a usable experience, not just a successful connection.
Something is on the screen
Text and a logo may already be visible
Some work may still be in progress
Appearance alone does not prove every feature works
The visitor can do the job
Links and controls respond
Needed information is available
An action may start another request-and-response cycle
Notes: DELIVERY: content; source Block A, slide 19.

## Slide 20
W01·A The whole journey
CSC 436 — Web Application Systems
20 / 90
Three milestones, not one checkbox
What the student observes | What it establishes | What it does not establish
Wi-Fi says connected | A local connection | Access to every Internet destination
Another website opens | At least one usable path and service | DePaul's site is available
DePaul's home page appears | Enough work completed to display it | Every link and feature is usable
Notes: DELIVERY: content; source Block A, slide 20.

## Slide 21
W01·A The whole journey
CSC 436 — Web Application Systems
21 / 90
Mac or Windows: the same jobs
◆ KEY IDEA
Later examples include Windows PowerShell and macOS Terminal (zsh or bash). Follow your OS, not both.
What stays the same
Join and configure a network connection
Find and communicate with the site
Receive resources, display a page, and respond to the user
What can look different
Settings screens and permission prompts
Terminal commands and diagnostic output
Browser menus and developer tools
Notes: DELIVERY: content; source Block A, slide 21.

## Slide 22
W01·A The whole journey
CSC 436 — Web Application Systems
22 / 90
From 'I can visit a website' to 'I can explain and operate what makes a web application work.'
— The course destination
Notes: DELIVERY: content; source Block A, slide 22.

## Slide 23
W01·A The whole journey
CSC 436 — Web Application Systems
23 / 90
◇ ACTIVE CHECKPOINT
10 min · Solo (3 min) → self-check against the model map (4 min) → instructor debrief (3 min)
Tell the story without the tools
Draw the journey from joining Wi-Fi to using DePaul's home page. Include the computer, local network, Internet, and website.
Mark one job before the page request and one job after the first response arrives.
Why can "Wi-Fi connected" be true while the page is not usable?
Notes: DELIVERY: content; source Block A, slide 23.

## Slide 24
W01·B On the network
CSC 436 — Web Application Systems
24 / 90
Getting on the network
How a machine acquires an identity, finds its neighbours, and reaches everything else — and why none of it is visible from your source code
Block A mapped the whole visit. Now we zoom into its first stages: joining and using the local network. Before your application communicates, the computer needs an identity, a local map, a way out, and help finding names.
Notes: DELIVERY: content; source Block B, slide 1.

## Slide 25
W01·B On the network
CSC 436 — Web Application Systems
25 / 90
Fictional CampusPulse case: reachable from here, invisible from there
Maya's laptop
DHCP assigns 10.24.18.73/20
The gateway is 10.24.16.1; DNS is 10.20.0.53
CampusPulse answers at localhost:8080
Luis's laptop
curl to 10.24.18.73:8080 gets connection refused
The listener table reveals 127.0.0.1:8080, not the Wi-Fi address
One bind setting, not the React code, decides who can connect
Notes: DELIVERY: content; source Block B, slide 2.

## Slide 26
W01·B On the network
CSC 436 — Web Application Systems
26 / 90
Four questions, answered before your code exists
Who am I? — an address this machine is allowed to use
Who is nearby? — which addresses it can reach without help
How do I get out? — where to send everything else
Who answers names? — which server turns text into an address
◆ KEY IDEA
Your application answers none of these. It inherits all four answers, from a
server it never authenticated to, over a protocol it never chose.
Notes: DELIVERY: content; source Block B, slide 3.

## Slide 27
W01·B On the network
CSC 436 — Web Application Systems
27 / 90
Four words about joining a local network
Term | Plain meaning
DHCP | The protocol a network uses to hand a newly joined device its address and settings.
Lease | The time-limited grant of that address. It expires, is renewed, and can change.
MAC address | A hardware address burned into a network adapter. Used only within one local network.
ARP | The "who has this address?" question a device shouts locally to find a neighbour's MAC address.
◆ KEY IDEA
DHCP gives a new device its starting information. ARP then helps it find another device on the same local network.
Notes: DELIVERY: content; source Block B, slide 4.

## Slide 28
W01·B On the network
CSC 436 — Web Application Systems
28 / 90
Four words about choosing the next hop
Term | Plain meaning
Subnet mask | The rule that says which addresses count as local neighbours and which do not.
CIDR (/20) | A shorthand for that same rule: how many leading bits of the address identify the network.
On-link | A destination you can reach directly, without asking the gateway to forward it.
Gateway | The device you hand traffic to when the destination is not on-link.
◆ KEY IDEA
Every mechanism in the next fifteen minutes is one of these eight words in action. You are not expected to know them yet.
Notes: DELIVERY: content; source Block B, slide 5.

## Slide 29
W01·B On the network
CSC 436 — Web Application Systems
29 / 90
What your machine will tell you
Windows ipconfig /all - captured and sanitized CONSOLE
Physical Address. . . . . : 00-0D-3A-XX-XX-XX # layer 2 identity
DHCP Enabled. . . . . . . : Yes # <- negotiated
IPv4 Address. . . . . . . : 10.0.20.252 # 1. who am I
Subnet Mask . . . . . . . : 255.255.128.0 # 2. who is nearby
Default Gateway . . . . . : 10.0.0.1 # 3. how do I get out
DHCP Server . . . . . . . : 168.63.129.16 # who told me all this
DNS Servers . . . . . . . : 10.0.254.4 # 4. who answers names
◆ KEY IDEA
Gateway, DHCP server, resolver: three different jobs. A home router may do
all three, but they need not share an address.
Course — full annotated capture · Microsoft — what 168.63.129.16 is
Notes: DELIVERY: content; source Block B, slide 6. SOURCES: Course — [full annotated capture](../samples/network-config.txt) Microsoft — [what 168.63.129.16 is](https://learn.microsoft.com/en-us/azure/virtual-network/what-is-ip-address-168-63-129-16)

## Slide 30
W01·B On the network
CSC 436 — Web Application Systems
30 / 90
Windows: inspect the active connection
Windows PowerShell - any directory; read-only POWERSHELL
ipconfig /all
Get-NetIPConfiguration
◆ KEY IDEA
Find the active adapter's address, prefix or mask, gateway, and DNS servers. Do not copy the sample's addresses.
Microsoft — Get-NetIPConfiguration
Notes: DELIVERY: content; source Block B, slide 7. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. ipconfig /all Get-NetIPConfiguration SOURCES: Microsoft — [Get-NetIPConfiguration](https://learn.microsoft.com/powershell/module/nettcpip/get-netipconfiguration)

## Slide 31
W01·B On the network
CSC 436 — Web Application Systems
31 / 90
macOS: find the interface and address
macOS Terminal - Bash/zsh; any directory; read-only BASH
networksetup -listallhardwareports
printf 'Device for active Wi-Fi/Ethernet (from list): '
read -r iface
ipconfig getifaddr "$iface"
ipconfig getpacket "$iface"
ifconfig "$iface"
◆ KEY IDEA
Do not assume Wi-Fi is en0. Match the hardware port to its Device entry.
Notes: DELIVERY: content; source Block B, slide 8. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. networksetup -listallhardwareports printf 'Device for active Wi-Fi/Ethernet (from list): ' read -r iface ipconfig getifaddr "$iface" ipconfig getpacket "$iface" ifconfig "$iface"

## Slide 32
W01·B On the network
CSC 436 — Web Application Systems
32 / 90
macOS lease fields: the same questions
These fields describe the last IPv4 DHCP response, not every current policy.
Field in getpacket | Same question as the Windows capture
yiaddr | Which IPv4 address was supplied?
subnet_mask | Which destinations are local?
router | Which gateway was supplied?
domain_name_server | Which name servers were supplied?
Notes: DELIVERY: content; source Block B, slide 9.

## Slide 33
W01·B On the network
CSC 436 — Web Application Systems
33 / 90
macOS: find the gateway and resolvers
macOS Terminal - Bash/zsh; any directory; read-only BASH
route -n get default
scutil --dns
◆ KEY IDEA
Read gateway and interface in the route; read nameserver and scope in the resolver configuration.
Notes: DELIVERY: content; source Block B, slide 10. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. route -n get default scutil --dns

## Slide 34
W01·B On the network
CSC 436 — Web Application Systems
34 / 90
How the address arrives: DISCOVER, OFFER, REQUEST, ACK
DHCP DORA — four messages, two of them broadcast, before the machine has an address to be addressed by
IETF — RFC 2131 §3.1, DHCP client-server interaction
Notes: DELIVERY: content; source Block B, slide 11. SOURCES: IETF — [RFC 2131 §3.1, DHCP client-server interaction](https://www.rfc-editor.org/rfc/rfc2131.html)

## Slide 35
W01·B On the network
CSC 436 — Web Application Systems
35 / 90
The lease is not just an address
Address + mask — identity, and the definition of "nearby"
Default gateway — the way out
DNS servers — who resolves names, which is a trust decision made for you
Lease duration — this is a rental, and it expires
NTP, domain, search suffix, routes — options nobody reads until one breaks
▲ WATCH OUT
A lease that never expires is not normal. On the capture above it ran to the year
2162 — a platform artifact of a cloud VM. A home router hands out 12 or 24 hours.
Notes: DELIVERY: content; source Block B, slide 12.

## Slide 36
W01·B On the network
CSC 436 — Web Application Systems
36 / 90
ARP: the frame needs a different address
The problem
The packet is addressed to 10.0.19.7. The frame needs a MAC.
So the host broadcasts "who has 10.0.19.7?" and caches the reply.
The reality on a cloud network
Real arp -a: 10.0.0.1, 10.0.0.63, 10.0.1.52, 10.0.7.77 — all four
map to the same MAC.
No shared wire; the fabric answers for everything.
▸ NOTE
IPv6 replaces ARP with NDP. Same job.
IETF — RFC 826, Address Resolution Protocol · RFC 4861, Neighbor Discovery
Notes: DELIVERY: content; source Block B, slide 13. SOURCES: IETF — [RFC 826, Address Resolution Protocol](https://www.rfc-editor.org/rfc/rfc826.html) · [RFC 4861, Neighbor Discovery](https://www.rfc-editor.org/rfc/rfc4861.html)

## Slide 37
W01·B On the network
CSC 436 — Web Application Systems
37 / 90
Which addresses can exist in public
CIDR | Where it works | You will meet it
10.0.0.0/8 | private only | cloud VNets, campus
172.16.0.0/12 | private only | Docker, WSL
192.168.0.0/16 | private only | home routers
127.0.0.0/8 | this machine only | the whole problem
169.254.0.0/16 | link-local | DHCP failed; cloud metadata
fe80::/10 | link-local IPv6 | every IPv6 interface
IETF — RFC 1918, private address allocation · RFC 3927, IPv4 link-local
Notes: DELIVERY: content; source Block B, slide 14. SOURCES: IETF — [RFC 1918, private address allocation](https://www.rfc-editor.org/rfc/rfc1918.html) · [RFC 3927, IPv4 link-local](https://www.rfc-editor.org/rfc/rfc3927.html)

## Slide 38
W01·B On the network
CSC 436 — Web Application Systems
38 / 90
CIDR: how many bits are the network?
255.255.128.0 is /17 — worked from the real capture TEXT
255.255.128.0 = 11111111 11111111 1000 0000 00000000
|--- 17 network ---|---- 15 host ----|
2^15 = 32,768 addresses 10.0.0.0 -> 10.0.127.255
10.0.19.7 in the /17 -> on-link, ARP for it
10.0.200.4 NOT in the /17 -> hand it to the gateway
8.8.8.8 nowhere near -> hand it to the gateway
◆ KEY IDEA
The mask is the if-statement your machine runs on every outbound packet: on-link, or hand it to the gateway?
Notes: DELIVERY: content; source Block B, slide 15.

## Slide 39
W01·B On the network
CSC 436 — Web Application Systems
39 / 90
The route table is that if-statement
Windows route print -4 - trimmed; most specific prefix wins CONSOLE
Destination Gateway Meaning
0.0.0.0/0 10.0.0.1 default route
10.0.0.0/17 On-link local campus subnet
127.0.0.0/8 On-link loopback
169.254.169.254/32 10.0.0.1 one pinned host
to 10.0.19.7 -> /17 -> ARP for it directly
to 8.8.8.8 -> /0 -> frame to gateway; IP stays 8.8.8.8
to 127.0.0.1 -> /8 -> never leaves the kernel
Course — annotated route table
Notes: DELIVERY: content; source Block B, slide 16. SOURCES: Course — [annotated route table](../samples/network-config.txt)

## Slide 40
W01·B On the network
CSC 436 — Web Application Systems
40 / 90
Windows: routes and nearby addresses
Windows PowerShell - any directory; inspection only POWERSHELL
route print -4
arp -a
Get-NetNeighbor -AddressFamily IPv6
◆ KEY IDEA
Routes choose the next hop. Neighbor entries map nearby network addresses to link addresses.
Microsoft — Get-NetNeighbor
Notes: DELIVERY: content; source Block B, slide 17. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. route print -4 arp -a Get-NetNeighbor -AddressFamily IPv6 SOURCES: Microsoft — [Get-NetNeighbor](https://learn.microsoft.com/powershell/module/nettcpip/get-netneighbor)

## Slide 41
W01·B On the network
CSC 436 — Web Application Systems
41 / 90
macOS: routes and nearby addresses
macOS Terminal - Bash/zsh; any directory; inspection only BASH
netstat -rn -f inet
route -n get default
arp -a
ndp -an
◆ KEY IDEA
Compare Destination, Gateway, and Netif; use ARP for IPv4 neighbors and NDP for IPv6.
Notes: DELIVERY: content; source Block B, slide 18. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. netstat -rn -f inet route -n get default arp -a ndp -an

## Slide 42
W01·B On the network
CSC 436 — Web Application Systems
42 / 90
Four words about reaching the Internet
Term | Plain meaning
Private address | An address usable only inside one network. Many networks reuse the same private ranges.
Public address | A globally unique address that the rest of the Internet can route to.
NAT | Rewriting private addresses into one shared public address on the way out, and back on the way in.
Port | A number that says which program on a machine a message is for.
◆ KEY IDEA
A home or campus network can use private addresses inside, then use NAT to share one public address when it talks to the Internet.
Notes: DELIVERY: content; source Block B, slide 19.

## Slide 43
W01·B On the network
CSC 436 — Web Application Systems
43 / 90
Four words about a program's connection
Term | Plain meaning
Socket | One end of a conversation: an address plus a port.
Listening socket | A program waiting for connections on a port.
Connected socket | An established conversation between two specific address-and-port pairs.
Bind address | The address a program agrees to accept connections on. 127.0.0.1 means "this machine only".
◆ KEY IDEA
127.0.0.1 (also called localhost, or loopback) never leaves your machine. 0.0.0.0 means "accept on every address I have".
Notes: DELIVERY: content; source Block B, slide 20.

## Slide 44
W01·B On the network
CSC 436 — Web Application Systems
44 / 90
NAT: the address you have is not the address you are
One public address, many private machines, and a translation table only you can open
Notes: DELIVERY: content; source Block B, slide 21.

## Slide 45
W01·B On the network
CSC 436 — Web Application Systems
45 / 90
The same request, from both ends
 | this host believes | the server received
address | 10.0.20.252 | 203.0.113.181
port | 49302 | 55346
■ THIS BREAKS PRODUCTION
Address and port were rewritten in flight — and a second run seconds later left
from
203.0.113.183. The egress is a pool, not a box.
Course — the full NAT capture · IETF — RFC 3022, Traditional NAT and NAPT
Notes: DELIVERY: content; source Block B, slide 22. SOURCES: Course — [the full NAT capture](../samples/path-and-nat.txt) IETF — [RFC 3022, Traditional NAT and NAPT](https://www.rfc-editor.org/rfc/rfc3022.html)

## Slide 46
W01·B On the network
CSC 436 — Web Application Systems
46 / 90
Ports and sockets: two tuples, and the difference matters
A listening socket is (address, port) — two values, e.g. 0.0.0.0:8471
A connected socket is (local addr, local port, remote addr, remote port) — four
The four-tuple is why one server port serves thousands of clients unambiguously
The client never chose its port; the kernel took one from the ephemeral range
TIME_WAIT is that four-tuple being held after close, not a leak
◆ KEY IDEA
A socket is an address and a port. If you got the address wrong, the port was
never the problem.
Notes: DELIVERY: content; source Block B, slide 23.

## Slide 47
W01·B On the network
CSC 436 — Web Application Systems
47 / 90
One listener, many conversations
netstat -ano, captured during a live request CONSOLE
Proto Local Address Foreign Address State
TCP 0.0.0.0:8471 0.0.0.0:0 LISTENING 25224
TCP 10.0.20.252:62681 10.0.20.252:8471 TIME_WAIT 0
TCP 10.0.20.252:62684 10.0.20.252:8471 TIME_WAIT 0
TCP 127.0.0.1:62630 127.0.0.1:8471 TIME_WAIT 0
row 1 TWO values: (0.0.0.0, 8471) <- the listener
rows 2+ FOUR values: (local, 62681, remote, 8471)
server side identical; the CLIENT ports differ
Course — full socket capture
Notes: DELIVERY: content; source Block B, slide 24. SOURCES: Course — [full socket capture](../samples/sockets-and-ports.txt)

## Slide 48
W01·B On the network
CSC 436 — Web Application Systems
48 / 90
One machine, one port, two answers
only the bind address changes CONSOLE
# bound to 127.0.0.1
TCP 127.0.0.1:8471 LISTENING
curl 127.0.0.1:8471 -> campuspulse ok
curl 10.0.20.252:8471 -> Connection refused (same box)
# rebound to 0.0.0.0 — no code changed
TCP 0.0.0.0:8471 LISTENING
curl 127.0.0.1:8471 -> campuspulse ok
curl 10.0.20.252:8471 -> campuspulse ok
Course — the full transcript
Notes: DELIVERY: content; source Block B, slide 25. SOURCES: Course — [the full transcript](../samples/sockets-and-ports.txt)

## Slide 49
W01·B On the network
CSC 436 — Web Application Systems
49 / 90
▶ LIVE DEMO
Break it live, in ninety seconds
DO THIS
Open A and B at the repo root; choose your OS steps; Node 18+
Run the loopback-only server and the two requests on the next slides
Stop it, bind all interfaces, and repeat without changing the URL
WATCH FOR
Loopback: JSON; LAN request fails
Wildcard: JSON on both if allowed
IF IT FAILS
Open the socket capture on the cleanup slide.
Course — the stub server
Notes: DELIVERY: content; source Block B, slide 26. SOURCES: Course — [the stub server](../samples/campuspulse-stub.mjs)

## Slide 50
W01·B On the network
CSC 436 — Web Application Systems
50 / 90
Windows A: bind only to loopback
Windows PowerShell - repository root; keep Terminal A running POWERSHELL
node --version
node .\weeks\week01\samples\campuspulse-stub.mjs 127.0.0.1 8471
▸ NOTE
Expect: campuspulse listening on 127.0.0.1:8471.
Course — stub arguments and response fields
Notes: DELIVERY: content; source Block B, slide 27. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. node --version node .\weeks\week01\samples\campuspulse-stub.mjs 127.0.0.1 8471 SOURCES: Course — [stub arguments and response fields](../samples/campuspulse-stub.mjs)

## Slide 51
W01·B On the network
CSC 436 — Web Application Systems
51 / 90
macOS A: bind only to loopback
macOS Terminal - Bash/zsh; repository root; Node 18+ BASH
node --version
node ./weeks/week01/samples/campuspulse-stub.mjs 127.0.0.1 8471
◆ KEY IDEA
Expect "campuspulse listening on 127.0.0.1:8471". Keep this terminal running.
Notes: DELIVERY: content; source Block B, slide 28. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. node --version node ./weeks/week01/samples/campuspulse-stub.mjs 127.0.0.1 8471

## Slide 52
W01·B On the network
CSC 436 — Web Application Systems
52 / 90
Windows B: ask two different addresses
Windows PowerShell - Terminal B; choose YOUR active LAN IPv4 POWERSHELL
ipconfig
$lan = Read-Host 'Active LAN IPv4, not 127.0.0.1'
Get-NetTCPConnection -State Listen -LocalPort 8471 |
Select-Object LocalAddress, LocalPort, OwningProcess
curl.exe --noproxy '*' -sS --max-time 3 http://127.0.0.1:8471/healthz
curl.exe --noproxy '*' -sS --max-time 3 "http://${lan}:8471/healthz"
$LASTEXITCODE
Microsoft — Get-NetTCPConnection · Course — socket evidence
Notes: DELIVERY: content; source Block B, slide 29. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. ipconfig $lan = Read-Host 'Active LAN IPv4, not 127.0.0.1' Get-NetTCPConnection -State Listen -LocalPort 8471 | Select-Object LocalAddress, LocalPort, OwningProcess curl.exe --noproxy '*' -sS --max-time 3 http://127.0.0.1:8471/healthz curl.exe --noproxy '*' -sS --max-time 3 "http://${lan}:8471/healthz" $LASTEXITCODE SOURCES: Microsoft — [`Get-NetTCPConnection`](https://learn.microsoft.com/powershell/module/nettcpip/get-nettcpconnection) Course — [socket evidence](../samples/sockets-and-ports.txt)

## Slide 53
W01·B On the network
CSC 436 — Web Application Systems
53 / 90
macOS B: ask two different addresses
macOS Terminal - Bash/zsh; Terminal B; active LAN IPv4 required BASH
networksetup -listallhardwareports
printf 'Active LAN Device from list: '; read -r iface
lan=$(ipconfig getifaddr "$iface")
printf 'LAN IPv4: %s\n' "$lan"
# If blank, stop here and use the offline comparison.
lsof -nP -iTCP:8471 -sTCP:LISTEN
curl --noproxy '*' -sS --max-time 3 http://127.0.0.1:8471/healthz
curl --noproxy '*' -sS --max-time 3 "http://${lan}:8471/healthz"
printf 'exit=%s\n' "$?"
Notes: DELIVERY: content; source Block B, slide 30. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. networksetup -listallhardwareports printf 'Active LAN Device from list: '; read -r iface lan=$(ipconfig getifaddr "$iface") printf 'LAN IPv4: %s\n' "$lan" # If blank, stop here and use the offline comparison. lsof -nP -iTCP:8471 -sTCP:LISTEN curl --noproxy '*' -sS --max-time 3 http://127.0.0.1:8471/healthz curl --noproxy '*' -sS --max-time 3 "http://${lan}:8471/healthz" printf 'exit=%s\n' "$?"

## Slide 54
W01·B On the network
CSC 436 — Web Application Systems
54 / 90
Windows A: change just the listener
Windows PowerShell - after Ctrl+C in A; repository root POWERSHELL
node .\weeks\week01\samples\campuspulse-stub.mjs 0.0.0.0 8471
▸ NOTE
Now repeat the socket query and both curl requests from the previous slide, unchanged.
▲ WATCH OUT
Use a trusted lab network. This exposes the synthetic stub on every IPv4 interface.
Course — stub server
Notes: DELIVERY: content; source Block B, slide 31. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. node .\weeks\week01\samples\campuspulse-stub.mjs 0.0.0.0 8471 SOURCES: Course — [stub server](../samples/campuspulse-stub.mjs)

## Slide 55
W01·B On the network
CSC 436 — Web Application Systems
55 / 90
macOS A: change just the listener
macOS Terminal - Bash/zsh; after Ctrl+C in A; repository root BASH
node ./weeks/week01/samples/campuspulse-stub.mjs 0.0.0.0 8471
▸ NOTE
In B, repeat lsof and both curl requests. Expect a wildcard listener and, if policy permits, two JSON replies.
▲ WATCH OUT
Use a trusted lab network. The synthetic stub now listens on every IPv4 interface.
Notes: DELIVERY: content; source Block B, slide 32. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. node ./weeks/week01/samples/campuspulse-stub.mjs 0.0.0.0 8471

## Slide 56
W01·B On the network
CSC 436 — Web Application Systems
56 / 90
What changed for Maya and Luis?
Observation | Mechanism | Safe conclusion
boundTo changes | The listener accepts more destination addresses | The bind configuration changed
servedOn differs | Each request chose an interface address | Same process, two local paths
peer port differs | Each client connection gets a source port | A request is not just a URL
Luis still cannot connect | Another boundary may block ingress | Check policy before changing code
Course — response fields
Notes: DELIVERY: content; source Block B, slide 33. SOURCES: Course — [response fields](../samples/campuspulse-stub.mjs)

## Slide 57
W01·B On the network
CSC 436 — Web Application Systems
57 / 90
Windows: stop the stub, keep the evidence
Windows PowerShell - Terminal B; repository root; offline POWERSHELL
Get-Content .\weeks\week01\samples\sockets-and-ports.txt
◆ KEY IDEA
Press Ctrl+C in Terminal A to stop the all-interface listener.
Notes: DELIVERY: content; source Block B, slide 34. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. Get-Content .\weeks\week01\samples\sockets-and-ports.txt

## Slide 58
W01·B On the network
CSC 436 — Web Application Systems
58 / 90
macOS: stop the stub, keep the evidence
macOS Terminal - Bash/zsh; Terminal B; repository root; offline BASH
cat ./weeks/week01/samples/sockets-and-ports.txt
◆ KEY IDEA
Ctrl+C in Terminal A stops the server. The saved Windows/Linux output is reference evidence, not today's Mac output.
Notes: DELIVERY: content; source Block B, slide 35. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. cat ./weeks/week01/samples/sockets-and-ports.txt

## Slide 59
W01·B On the network
CSC 436 — Web Application Systems
59 / 90
Why "it works on localhost" means nothing
127.0.0.0/8 is matched in the route table and handed back to the kernel
It does not cross the physical LAN, its router, or its NAT
A successful loopback request tests the app and a local path, not remote ingress
A private address needs an explicit external path; NAPT may also rewrite its port
Every one of those is a thing a reviewer, a friend testing your app, and your users are on the other side of
■ THIS BREAKS PRODUCTION
"It works on my machine" is not a lie. It is a true statement about a code path
that shares almost nothing with the one your users take.
Notes: DELIVERY: content; source Block B, slide 36.

## Slide 60
W01·B On the network
CSC 436 — Web Application Systems
60 / 90
◇ ACTIVE CHECKPOINT
10 min · Solo (4 min) → cold call (3 min) → debrief (3 min)
A service works for Priya, but not for Dev. Three artifacts. Diagnose it.
A) Priya runs: netstat -ano | findstr :8080
TCP 127.0.0.1:8080 0.0.0.0:0 LISTENING 9134
B) Dev runs: curl --max-time 5 http://192.168.1.47:8080/healthz
curl: (7) Failed to connect ... Connection refused
C) Dev runs: curl --max-time 5 http://192.168.1.47:3000/ -> 200 OK
1. What is the cause? 2. Which artifact rules out a completely broken path? 3. Priya says "let's just use port 80." What happens?
Course — supplied failure prompt and artifacts
Notes: DELIVERY: content; source Block B, slide 37. SOURCES: Course — [supplied failure prompt and artifacts](../samples/injected-failures/failure-01-refused-from-lan/README.md)

## Slide 61
W01·C The URL chain
CSC 436 — Web Application Systems
61 / 90
Transport and the URL chain
TCP, UDP, and QUIC — then every link between pressing Enter and seeing a pixel, which is the map the rest of this course is drawn on
Block B got you an address. This block is about what happens after you have one — and then about the twelve steps between pressing Enter and seeing a pixel, which is the map for the next nine weeks.
Notes: DELIVERY: content; source Block C, slide 1.

## Slide 62
W01·C The URL chain
CSC 436 — Web Application Systems
62 / 90
Fictional CampusPulse case: the spinner does not tell you which link failed
What Maya sees
She taps Report outage on the train
The spinner runs for two seconds, then the page says "Try again"
Her first diagnosis: "the server is down"
What the evidence says
DNS 18 ms; TCP 24 ms; TLS 51 ms
HTTP returns 200 with JSON in 140 ms
The browser console shows a JavaScript exception after the bytes arrive
Notes: DELIVERY: content; source Block C, slide 2.

## Slide 63
W01·C The URL chain
CSC 436 — Web Application Systems
63 / 90
Four words about starting a connection
Term | Plain meaning
Protocol | An agreed set of rules two machines follow so each one understands the other.
TCP | The protocol that gives you an ordered, reliable stream of bytes between two programs.
Handshake | The short exchange that sets up a connection before any useful data is sent.
Round trip (RTT) | The time for a message to reach the other side and its reply to come back.
◆ KEY IDEA
Before a browser can ask for a page, its connection follows a protocol and usually completes a handshake. RTT measures the wait for one exchange.
Notes: DELIVERY: content; source Block C, slide 3.

## Slide 64
W01·C The URL chain
CSC 436 — Web Application Systems
64 / 90
Four words about keeping a connection safe
Term | Plain meaning
Sequence number | A counter on each byte, so the receiver can reorder and detect what is missing.
Retransmission | Sending data again because it was not acknowledged in time.
TLS | The layer that encrypts an HTTPS conversation and proves you reached the real site.
Reset (RST) | An abrupt "stop, this connection is over" from the other end.
◆ KEY IDEA
TCP uses sequence numbers and retransmissions to keep data reliable. TLS makes that data private. A reset ends the conversation abruptly.
Notes: DELIVERY: content; source Block C, slide 4.

## Slide 65
W01·C The URL chain
CSC 436 — Web Application Systems
65 / 90
TCP: nobody speaks until both sides have agreed to
Three packets and one round trip before either side may send a single useful byte
IETF — RFC 9293, Transmission Control Protocol
Notes: DELIVERY: content; source Block C, slide 5. SOURCES: IETF — [RFC 9293, Transmission Control Protocol](https://www.rfc-editor.org/rfc/rfc9293.html)

## Slide 66
W01·C The URL chain
CSC 436 — Web Application Systems
66 / 90
What TCP gives you, and what it charges
Ordering — segments carry sequence numbers, so the receiver reassembles the stream
Retransmission — an unacknowledged segment is sent again, with exponential backoff
Flow control — the receiver advertises a window, so a fast sender cannot drown a slow one
Congestion control — the sender backs off when the network is the bottleneck
The bill: one round trip of setup, per-connection state on both ends, and head-of-line blocking
◆ KEY IDEA
TCP turns an unreliable packet network into a reliable byte stream. Everything on
this list is the price of that sentence.
Notes: DELIVERY: content; source Block C, slide 6.

## Slide 67
W01·C The URL chain
CSC 436 — Web Application Systems
67 / 90
Sequencing and retransmission: how silence is handled
A lost segment is detected by a gap, not by an error — and the retry interval doubles
Notes: DELIVERY: content; source Block C, slide 7.

## Slide 68
W01·C The URL chain
CSC 436 — Web Application Systems
68 / 90
Ending a connection: politely, or not
FIN — the orderly close
Four packets. Either side may stop sending and keep receiving, so the close
is half-duplex first.
TIME_WAIT then holds the four-tuple for 2 × MSL.
RST — the abort
One packet. No agreement, unread data discarded.
A FIN is an agreement. A RST is a decision.
▲ WATCH OUT
Many TIME_WAIT sockets are normal; exhaustion needs evidence of failed new connections.
IETF — RFC 9293 §3.6, closing a connection
Notes: DELIVERY: content; source Block C, slide 8. SOURCES: IETF — [RFC 9293 §3.6, closing a connection](https://www.rfc-editor.org/rfc/rfc9293.html)

## Slide 69
W01·C The URL chain
CSC 436 — Web Application Systems
69 / 90
Four symptoms: read the failure, not just the code
same tool, four different layers CONSOLE
127.0.0.1:9 -> (7) refused: RST, host answered no
192.0.2.1 -> (28) timeout: silence, no answer
127.0.0.1:8472 -> (56) reset: request sent, then abort
example.com:443 -> (52) empty reply: orderly FIN
◆ KEY IDEA
In plain words: refused means something answered and said no. Timeout means nothing answered at all. Reset means a conversation had started and was cut off. Empty reply means the connection closed politely without sending an answer.
Course — the full transcripts and a decision table
Notes: DELIVERY: content; source Block C, slide 9. SOURCES: Course — [the full transcripts and a decision table](../samples/refused-vs-timeout.txt)

## Slide 70
W01·C The URL chain
CSC 436 — Web Application Systems
70 / 90
macOS A: reproduce a local reset
macOS Terminal - Bash/zsh; repository root; Node 18+ BASH
node ./weeks/week01/samples/abort-server.mjs 8472
◆ KEY IDEA
The loopback-only fixture accepts a connection, reads request bytes, then resets it. Keep A running.
Notes: DELIVERY: content; source Block C, slide 10. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. node ./weeks/week01/samples/abort-server.mjs 8472

## Slide 71
W01·C The URL chain
CSC 436 — Web Application Systems
71 / 90
Reproduce a local reset
Windows PowerShell - Terminal A; repository root; Node 18+ POWERSHELL
node .\weeks\week01\samples\abort-server.mjs 8472
Course — local reset fixture
Notes: DELIVERY: content; source Block C, slide 11. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. node .\weeks\week01\samples\abort-server.mjs 8472 SOURCES: Course — [local reset fixture](../samples/abort-server.mjs)

## Slide 72
W01·C The URL chain
CSC 436 — Web Application Systems
72 / 90
macOS B: find the last completed phase
macOS Terminal - Bash/zsh; same machine as Terminal A BASH
curl --noproxy '*' -v --max-time 5 http://127.0.0.1:8472/
printf 'exit=%s\n' "$?"
# Ctrl+C in A; repeat these two commands to compare.
◆ KEY IDEA
While A runs: connected, request sent, then a receive failure. After stopping A: connection fails earlier.
Notes: DELIVERY: content; source Block C, slide 12. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. curl --noproxy '*' -v --max-time 5 http://127.0.0.1:8472/ printf 'exit=%s\n' "$?" # Ctrl+C in A; repeat these two commands to compare.

## Slide 73
W01·C The URL chain
CSC 436 — Web Application Systems
73 / 90
Terminal B: locate the last successful phase
Windows PowerShell - same machine as Terminal A POWERSHELL
curl.exe --noproxy '*' -v --max-time 5 http://127.0.0.1:8472/
$LASTEXITCODE
# Now Ctrl+C in Terminal A; repeat both lines to compare.
curl — exit codes and verbose diagnostics · Course — reset fixture
Notes: DELIVERY: content; source Block C, slide 13. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. curl.exe --noproxy '*' -v --max-time 5 http://127.0.0.1:8472/ $LASTEXITCODE # Now Ctrl+C in Terminal A; repeat both lines to compare. SOURCES: curl — [exit codes and verbose diagnostics](https://curl.se/docs/manpage.html) Course — [reset fixture](../samples/abort-server.mjs)

## Slide 74
W01·C The URL chain
CSC 436 — Web Application Systems
74 / 90
Same spinner; a different next action
Last evidence | What happened | Next diagnostic
No Connected line | The connection did not establish | Inspect listener, destination, route
Connected, then outgoing GET | The server accepted the connection | Inspect reset/crash/proxy evidence
An HTTP status and headers | Transport carried an HTTP response | Read status, body, and app logs
A timeout after connecting | A later phase took too long | Locate the stalled phase; do not blame DNS
Course — failure decision table
Notes: DELIVERY: content; source Block C, slide 14. SOURCES: Course — [failure decision table](../samples/refused-vs-timeout.txt)

## Slide 75
W01·C The URL chain
CSC 436 — Web Application Systems
75 / 90
macOS: the same offline comparison
macOS Terminal - Bash/zsh; repository root; offline BASH
cat ./weeks/week01/samples/refused-vs-timeout.txt
◆ KEY IDEA
Ctrl+C in A stops the fixture. The archived output explains the phases; Mac error wording may differ.
Notes: DELIVERY: content; source Block C, slide 15. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. cat ./weeks/week01/samples/refused-vs-timeout.txt

## Slide 76
W01·C The URL chain
CSC 436 — Web Application Systems
76 / 90
Fallback and cleanup: no firewall experiment
Windows PowerShell - repository root; archived evidence POWERSHELL
Get-Content .\weeks\week01\samples\refused-vs-timeout.txt
◆ KEY IDEA
Stop Terminal A with Ctrl+C. Do not create a DROP rule to force a timeout.
Notes: DELIVERY: content; source Block C, slide 16. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. Get-Content .\weeks\week01\samples\refused-vs-timeout.txt

## Slide 77
W01·C The URL chain
CSC 436 — Web Application Systems
77 / 90
UDP: no handshake, no memory
◆ KEY IDEA
UDP sends single messages, called datagrams, with no setup and no memory of what came before. It is not "broken TCP" — it is TCP with every guarantee removed, so the application can choose which ones it actually wants.
What it does not do
No connection, so no setup round trip
No ordering, no retransmission
No flow or congestion control
An 8-byte header, versus TCP's 20
When that is the right trade
DNS — 29 bytes; a retry beats a handshake
DHCP — you have no address yet
Audio and video — late is worse than lost
QUIC — rebuilds reliability on top
IETF — RFC 768, User Datagram Protocol
Notes: DELIVERY: content; source Block C, slide 17. SOURCES: IETF — [RFC 768, User Datagram Protocol](https://www.rfc-editor.org/rfc/rfc768.html)

## Slide 78
W01·C The URL chain
CSC 436 — Web Application Systems
78 / 90
QUIC: the handshake, rebuilt on UDP
Runs over UDP, then rebuilds ordering, retransmission, and congestion control above it
Merges the transport and TLS handshakes — 1 RTT to a new server; 0 RTT on a resumed
Streams are independent, so one lost packet no longer stalls the others
A connection ID lets a connection survive a network change, when both ends support it
HTTP/3 is HTTP over QUIC, and it is already a large share of real traffic
◆ KEY IDEA
QUIC is a newer transport that does TCP's job and TLS's job at the same time, carried inside UDP. RTT is a round trip; "1 RTT" means one there-and-back before real data flows. HTTP/3 is simply HTTP delivered over QUIC.
IETF — RFC 9000, QUIC transport · RFC 9114, HTTP/3
Notes: DELIVERY: content; source Block C, slide 18. SOURCES: IETF — [RFC 9000, QUIC transport](https://www.rfc-editor.org/rfc/rfc9000.html) · [RFC 9114, HTTP/3](https://www.rfc-editor.org/rfc/rfc9114.html)

## Slide 79
W01·C The URL chain
CSC 436 — Web Application Systems
79 / 90
The spine of this course
From URL to pixel
Notes: DELIVERY: content; source Block C, slide 19.

## Slide 80
W01·C The URL chain
CSC 436 — Web Application Systems
80 / 90
The chain
◆ KEY IDEA
Three of these names are new: an edge/CDN is a server placed near the user that can answer with a stored copy; the origin is the machine that actually owns the content; render is the browser turning HTML and CSS into pixels on screen.
Twelve links. Every remaining week of this course attaches to one of them.
Notes: DELIVERY: content; source Block C, slide 20.

## Slide 81
W01·C The URL chain
CSC 436 — Web Application Systems
81 / 90
The first six links, timed
Archived Windows curl run - cumulative seconds CONSOLE
$ curl -sS -o NUL -w "dns=%{time_namelookup} tcp=%{time_connect}
tls=%{time_appconnect} ttfb=%{time_starttransfer}
total=%{time_total}\n" https://www.depaul.edu/
dns=0.010978 tcp=0.013690 tls=0.246471 ttfb=0.622437 total=0.647152
link 3 DNS 11 ms cached; a cold lookup is 20-120 ms
link 4 TCP handshake + 3 ms one round trip, close by
link 5 TLS handshake + 233 ms the most expensive thing here
links 6-8 request, edge, origin, first byte + 376 ms
the remaining 238 KB of body + 25 ms
◆ KEY IDEA
Four numbers localise a slow page to a link — no profiler, no dashboard, and it
runs anywhere
curl runs.
curl manual — --write-out variables
Notes: DELIVERY: content; source Block C, slide 21. SOURCES: [curl manual — `--write-out` variables](https://curl.se/docs/manpage.html)

## Slide 82
W01·C The URL chain
CSC 436 — Web Application Systems
82 / 90
Windows: measure those same phases
Windows PowerShell - any directory; internet required POWERSHELL
$fmt = 'dns=%{time_namelookup} tcp=%{time_connect} '
$fmt += 'tls=%{time_appconnect} ttfb=%{time_starttransfer} '
$fmt += 'total=%{time_total}\n'
curl.exe -sS -o NUL --max-time 15 -w $fmt https://www.depaul.edu/
◆ KEY IDEA
These are cumulative seconds, not five independent durations. Your values need not match the archived capture.
Notes: DELIVERY: content; source Block C, slide 22. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. $fmt = 'dns=%{time_namelookup} tcp=%{time_connect} ' $fmt += 'tls=%{time_appconnect} ttfb=%{time_starttransfer} ' $fmt += 'total=%{time_total}\n' curl.exe -sS -o NUL --max-time 15 -w $fmt https://www.depaul.edu/

## Slide 83
W01·C The URL chain
CSC 436 — Web Application Systems
83 / 90
macOS: measure those same phases
macOS Terminal - Bash/zsh; any directory; internet required BASH
fmt='dns=%{time_namelookup} tcp=%{time_connect} '
fmt="${fmt}tls=%{time_appconnect} ttfb=%{time_starttransfer} "
fmt="${fmt}total=%{time_total}\n"
curl -sS -o /dev/null --max-time 15 -w "$fmt" https://www.depaul.edu/
◆ KEY IDEA
Same fields and interpretation; /dev/null replaces Windows NUL. Keep the format variable quoted.
curl — write-out variables
Notes: DELIVERY: content; source Block C, slide 23. PLAIN-TEXT COMMANDS: Copy from here or the Markdown/HTML source; colored PowerPoint code uses nonbreaking spaces for layout. fmt='dns=%{time_namelookup} tcp=%{time_connect} ' fmt="${fmt}tls=%{time_appconnect} ttfb=%{time_starttransfer} " fmt="${fmt}total=%{time_total}\n" curl -sS -o /dev/null --max-time 15 -w "$fmt" https://www.depaul.edu/ SOURCES: curl — [write-out variables](https://curl.se/docs/manpage.html)

## Slide 84
W01·C The URL chain
CSC 436 — Web Application Systems
84 / 90
Four filters, four links, four artifacts
Link | Wireshark display filter | What you should find
3 · DNS | dns | one query, one response, 2 answers, a TTL
4 · TCP | tcp.flags.syn == 1 | exactly two packets: SYN, then SYN+ACK
5 · TLS | tls.handshake.type == 1 | your hostname, in cleartext
6 · HTTP | http.request | the Host: header — and nothing over HTTPS
Wireshark — display filter reference · Course — a fully worked annotated capture
Notes: DELIVERY: content; source Block C, slide 24. SOURCES: Wireshark — [display filter reference](https://www.wireshark.org/docs/wsug_html_chunked/ChWorkDisplayFilterSection.html) Course — [a fully worked annotated capture](../samples/capture-walkthrough.md)

## Slide 85
W01·C The URL chain
CSC 436 — Web Application Systems
85 / 90
One link failed. Everything looked down.
4 October 2021
A routine backbone maintenance
command was issued to
assess
capacity.
The audit tool had a bug.
Every Facebook data centre fell
off the internet.
What actually broke for users
The DNS servers were healthy, but
their health check could not reach
the data centres.
They withdrew their BGP routes.
■ THIS BREAKS PRODUCTION
Link 3 failed; every other link became unreachable.
Meta Engineering — More details about the October 4 outage (primary postmortem)
Notes: DELIVERY: content; source Block C, slide 25. SOURCES: Meta Engineering — [More details about the October 4 outage](https://engineering.fb.com/2021/10/05/networking-traffic/outage-details/) (primary postmortem)

## Slide 86
W01·C The URL chain
CSC 436 — Web Application Systems
86 / 90
Links 9 to 12: the bytes arrived, and nothing is on screen yet
Parse — HTML becomes a DOM; a blocking <script> in <head> stops the parser dead
Execute — JavaScript runs, and with client-side rendering nothing is visible until it finishes
Render — style, layout, paint, composite; this is where a11y and Core Web Vitals live
Interact — the page looks ready but the handlers are not attached yet, so clicks are dropped
▲ WATCH OUT
"Fast" is not one number. A page can reach first paint in 400 ms and be unusable
for three seconds. Users report the second one.
MDN — Navigation and resource timings
Notes: DELIVERY: content; source Block C, slide 26. SOURCES: MDN — [Navigation and resource timings](https://developer.mozilla.org/en-US/docs/Web/Performance/Guides/Navigation_and_resource_timings)

## Slide 87
W01·C The URL chain
CSC 436 — Web Application Systems
87 / 90
◇ ACTIVE CHECKPOINT
10 min · Solo (4 min) → cold call (3 min) → debrief (3 min)
Four users, four reports. Which link broke, and what evidence settles it?
"Server not found." Their colleague at the next desk loads it fine.
Padlock warning on a phone; fine on both laptops in the room.
Page loads instantly but shows yesterday's incident list.
Page paints in 300 ms; buttons do nothing for four seconds.
Course — the URL chain and which week owns each link
Notes: DELIVERY: content; source Block C, slide 27. SOURCES: Course — [the URL chain and which week owns each link](../../../docs/course-map.md)

## Slide 88
W01·C Individual practice
CSC 436 — Web Application Systems
88 / 90
Guided lab: capture your own traffic, then break your own port
Now, 35 minutes: find your machine's network settings, then capture a real page load
In the capture: point at the DNS query, the TCP handshake, the TLS ClientHello, and the first HTTP request
Then break it on purpose: stop your own listening port and diagnose refused vs. timed out vs. reset from symptoms alone
Evidence, not a screenshot: every step has a saved fallback capture for a restricted machine or VPN
◆ KEY IDEA
Full instructions and fallbacks: lab.md.
Notes: DELIVERY: practice; source Block C, slide 28.

## Slide 89
W01·C Homework brief
CSC 436 — Web Application Systems
89 / 90
HW1: the Packet-to-Pixel Evidence Dossier
Purpose: prove you can watch one page load happen and read the evidence, not guess at it
Deliverables: network config, an annotated packet capture, a HAR export, and a curl -v trace
Plus: a socket/port map, a hand-drawn sequence diagram, two diagnosed failures, and proof of domain purchase
Task 9, the non-generatable one: reject one AI claim about your own evidence, and show what disproves it
Buy your domain this week. Registrar verification and propagation are a third party's clock, not yours
100 points · individual · full handout and rubric: homework.md — due at the start of Week 2 class
✦ TIP
The domain hardship path is private, needs no explanation, and carries no grade difference. Ask, and it is done.
Course — HW1 handout · evidence standard
Notes: DELIVERY: homework; source Block C, slide 29. SOURCES: Course — [HW1 handout](../homework.md) · [evidence standard](../../../docs/evidence-standard.md)

## Slide 90
W01·C Closing logistics
CSC 436 — Web Application Systems
90 / 90
Before you go
Exit ticket: one sentence — what surprised you about today's journey, or where it still feels fuzzy
Bring to Week 2: your purchased domain and registrar login
Before Week 2 class: complete the Week 2 prep — five items, about 44 minutes, plus its readiness check
Any logistics question we didn't reach: the discussion board, not a hallway guess
Next week: the name you just bought becomes an address — resolution, in depth
Notes: DELIVERY: closing; source Block C, slide 30.